## Slide 1
Team 1
Line Follower Robot

## Slide 2
Line Follower Robot
Motor driver
Arduino
IR sensor
Signal sensor
Microcontroller
Movement controller
Power
Power Distribution

## Slide 3
L293D Motor Driver

## Slide 4
Enable 1,2
Controlling Motor 1 Speed
Input 1, Input 2
Controlling Motor 1 Direction
Output 1, Output 2
Connected to the controlled
motor
Vcc2
The voltage required for
the motors to work
4.5V:36V
Enable 3,4
Controlling Motor 2 Speed
Input 3, Input 4
Controlling Motor 2 Direction
Output 1, Output 2
Connected to the controlled
motor
Vcc1
5V for internal logic translation
L293D Motor Driver
Pins Diagram

## Slide 5
L293D Motor Driver
PCB
Controlled Motor #2
L293D IC
Controlled Motor #1
Motor #1 Controlling Data
In1, in2 -> direction
ENA -> speed
Motor #2 Controlling Data
In3, in4 -> direction
ENB -> speed
Fastening Holes
Power for circuit’s
Components
+5V, 0V, +12V

## Slide 6
IR Sensor

## Slide 7
TCRT5000 Sensor
Schematic circuit of TCRT5000
TCRT5000 sensor
LM358 OP-amp

## Slide 8
Pin header
LM358
led1
V-R
R1
R2
R3
Tcrt5000
Top layer
Bottom layer
PCB

## Slide 9
Power Distribution

## Slide 10
Power Distribution
On/Off Switch
Output 12V, 5V
Distributes Batteries power in order to be able to operate all robot’s parts
with the same battery
Fastening Holes
Output Indicating
LEDs
V-Reg 7805
Prevent Wrong
Connection
Input 12V

## Slide 11
Arduino Code

## Slide 12
Arduino UNO
Maximum input current 20mA
Maximum output current
40mA
Operating volte 5V
Input voltage
(recommended) 7-12V
Input voltage (limits) 6-20V
14 Digital I/O pins
(of which 6 provide PWM output)
6 analog input pins
Three power ways
Clock speed 16MHz
Microcontroller ATmega328

## Slide 13
Showing motors pins, sensors pins and define them
Movement functions
( showing how to control robot movement )

## Slide 14
Final Result

## Slide 15
Due to error in the downloaded sensor's library we replaced it in the simulation with logic states
Simulation schematic circuit

## Slide 16
Robot chassis

## Slide 17
Thank you